5VA Toroidal Power Transformer

1.Product characteristics:

  - General description:

This device is a power transformer for use in low voltage power supply applications. It shall include 230Volt 50hertz primary and dual 5Volt 1AC amp secondary. The device must meet all requirements outlined in this specification.

- Electrical specifications

2.1.Circuit diagram

2.2.Electrical performance

2.2.1.Rated primary voltage:0-230Vac

2.2.2.Rated frequency:50Hz

2.2.3.Rated output capacity:5VA

2.2.4.Secondary voltage deviation and regulation:

| Secondary | Output no-load voltage | Rated current | Output load voltage | Actual voltage regulation |
| --- | --- | --- | --- | --- |
|  | Rated | Actual measurement |  | Rated | Actual measurement |  |
| S1:3-4 | 5Vac±5％ | 5.07Vac±5％ | AC 1A | 4Vac±5％ | 4.3Vac±5％ | 15％ |

2.2.5.No-load current

The no load current shall current not exceed 5mA when a test voltage of 230V/50Hz is applied across the 220Vac primary input terminal.

2.2.6. No-load loss

The no-load loss shall not exceed 0.33Watt when a test voltage of 230V/50Hz is applie across the 230Vac primary input terminal.

# Text boxes

1.Red  0V

2.Red  230V

1A

3.Black   5V

4.Black    0V

The Picture Of  Installation

The Picture Of Form

H

D